## Slide 1: Sailplane Rule Book
Chapter 1 — Air operations
Chapter 2 — Licensing (reserved)
Chapter 3 — Continuing airworthiness (reserved)
Chapter 4 — Initial airworthiness

## Slide 2: Chapter 1 — Air operations [PART-SAO]
SUBPART GEN – GENERAL REQUIREMENTS
SUBPART OP – OPERATING PROCEDURES
SUBPART POL – PERFORMANCE AND OPERATING LIMITATIONS
SUBPART IDE – INSTRUMENTS, DATA AND EQUIPMENT
SUBPART DEC – DECLARATION

## Slide 3: SUBPART GEN – GENERAL REQUIREMENTS
(7) ‘introductory flight’ means any air operation with a sailplane against remuneration or other valuable consideration consisting of an air tour of short duration for the purpose of attracting new trainees or new members, performed either by a training organisation referred to in Article 10a of Commission Regulation (EU) No 1178/20112 or by an organisation created with the aim of promoting aerial sport or leisure aviation;
SAO.GEN.115 Introductory flights
Regulation (EU) 2018/1976
Introductory flights shall be:
(a) operated under visual flight rules (VFR) by day; and
(b) overseen as regards their safety by a person who has been nominated by the organisation responsible for the introductory flights.
12. ‘sailplane specialised operation’ means any operation, which can be commercial or non-commercial, with a sailplane the main purpose of which is not associated with typical sport and recreational operations, but parachute operations, news media flights, television or movie flights, flying display or similar specialised activities;

## Slide 4: SUBPART GEN – GENERAL REQUIREMENTS
SAO.GEN.125 Designation of the pilot-in-command
Regulation (EU) 2018/1976
The operator shall designate a pilot-in-command who is qualified to act as pilot-in-command in accordance with Annex I to Regulation (EU) No 1178/2011.
SAO.GEN.130 Responsibilities of the pilot-in-command
Regulation (EU) 2018/1976
The pilot-in-command shall:

## Slide 5: SUBPART GEN – GENERAL REQUIREMENTS
GM1 SAO.GEN.130(m) Responsibilities of the pilot-in-command
ED Decision 2019/001/R
RECORDING UTILISATION DATA
Where a sailplane conducts a series of flights of short duration, the utilisation data for the series of flights may be recorded in the aircraft technical log or journey log as a single entry.
GM2 SAO.GEN.130(m) Responsibilities of the pilot-in-command
ED Decision 2019/001/R
SERIES OF FLIGHTS
(a) ‘Series of flights’ refers to consecutive flights, which begin and end:
(1) within a 24-hour period; and
(2) at the same operating site or remain within a local area.
(b) The term ‘series of flights’ is used to facilitate a single set of documentation.

## Slide 6: SUBPART GEN – GENERAL REQUIREMENTS
SAO.GEN.145 Portable electronic devices
Regulation (EU) 2018/1976
The pilot-in-command shall not permit any person to use a portable electronic device (PED) on board a sailplane, including an electronic flight bag (EFB), that adversely affects the performance of the sailplane's systems and equipment or the ability to operate it.
GM1 SAO.GEN.145 Portable electronic devices
ED Decision 2019/001/R
CATEGORIES OF PORTABLE ELECTRONIC DEVICES
Portable electronic devices (PEDs) are any kind of electronic device, typically but not limited to consumer electronics, brought on board the sailplane by any person and that are not included in the approved sailplane configuration. All equipment that is able to consume electrical energy falls under this definition. The electrical energy can be provided from internal sources such as batteries (rechargeable or non-rechargeable) or the devices may also be connected to specific sailplane power sources.
PEDs include the following two categories:

## Slide 7: SUBPART GEN – GENERAL REQUIREMENTS
SAO.GEN.155 Documents, manuals and information to be carried
Regulation (EU) 2018/1976
(a) All of the following documents, manuals and information shall be carried on each flight as originals or copies:
(b) In addition, when a declaration is required in accordance with point SAO.DEC.100, a copy of the declaration shall be carried on each flight.
(c) When not carried on board, all of the following documents, manuals and information shall remain available at the aerodrome or operating site as originals or copies:
(1) the certificate of registration;
(2) the certificate of airworthiness, including the annexes;
(3) the airworthiness review certificate;
(5) the aircraft radio licence, where the sailplane is equipped with radio communication equipment in accordance with point SAO.IDE.130;
(6) the third-party liability insurance certificate(s);
(7) the journey log or equivalent.
(d) By derogation from points (a) and (b), the documents, manuals and information specified therein may be retained at the aerodrome or operating site for flights:
(1) intending to remain within the sight of the aerodrome or operating site; or
(2) remaining within a distance or area determined by the competent authority.

## Slide 8: SUBPART OP – OPERATING PROCEDURES
SAO.OP.110 Passenger briefing
Regulation (EU) 2018/1976
The pilot-in-command shall ensure that before and, when appropriate, during the flight, the passenger is given a briefing on normal, abnormal and emergency procedures.
AMC1 SAO.OP.155 Sailplane specialised operations
ED Decision 2019/001/R
CRITERIA FOR SAILPLANE SPECIALISED OPERATIONS
The pilot-in-command or the operator should consider the following criteria to determine whether an activity falls within the scope of sailplane specialised operations:
(a) special equipment affecting the behaviour of the sailplane in flight is necessary to fulfil the task; or
(b) persons leave the sailplane during flight.

## Slide 9: SUBPART OP – OPERATING PROCEDURES
GM1 SAO.OP.155 Sailplane specialised operations
ED Decision 2019/001/R
LIST OF OPERATIONS
(a) Sailplane specialised operations include the following activities:
(1) parachute operations;
(2) aerial advertising flights, i.e. banner towing with powered sailplanes;
(3) news media flights, television and movie flights; and
(4) flying display.
(b) The following operations are not considered sailplane specialised operations, but normal operations:
(1) sailplane towing;
(2) competition flights; and
(3) aerobatic flights.

## Slide 10: SUBPART POL – PERFORMANCE AND OPERATING LIMITATIONS
SAO.POL.100 Weighing
Regulation (EU) 2018/1976
(a) The weighing of the sailplane shall be accomplished by the manufacturer of the sailplane or in accordance with Annex I to Commission Regulation (EU) No 1321/20141.
(b) The operator shall ensure that the mass of the sailplane has been established by actual weighing prior to its initial entry into service. The accumulated effects of modifications and repairs on the mass shall be accounted for and properly documented. Such information shall be made available to the pilot-in-command. The sailplane shall be reweighed if the effects of modifications or repairs on the mass are not known.

## Slide 11: SUBPART IDE – INSTRUMENTS, DATA AND EQUIPMENT
SAO.IDE.100 Instruments and equipment – general
Regulation (EU) 2018/1976
(a) Instruments and equipment required by this Subpart shall be approved in accordance with Annex I to Regulation (EU) No 748/2012 or, when registered in a third country, with the airworthiness requirements of the state of registry, if one of the following conditions is fulfilled:
(1) they are used by the flight crew to control the flight path;
(2) they are used to comply with points SAO.IDE.130 or SAO.IDE.135;
(3) they are permanently installed in the sailplane.
(b) By way of derogation from point (a), all of the following instruments or equipment, when required by this Subpart, shall not need an approval:
(1) independent portable lights;
(2) an accurate timepiece;
(3) survival and signalling equipment.
(c) Instruments and equipment shall be readily operable or accessible from the station where either the pilot-in-command or any other crew member, who needs to use them, is seated.
GM1 SAO.IDE.100 Instruments and equipment – general
ED Decision 2019/001/R
INSTRUMENTS AND EQUIPMENT NOT REQUIRED
(a) Non-required instruments and equipment do not need to be approved in accordance with airworthiness requirements. However, their installation needs to be approved in accordance with these requirements, as part of which the instrument or equipment is accepted for installation on a non-hazard basis.
(b) The failure of additional, non-installed instruments or equipment not required by this Annex or by the applicable airworthiness requirements or any applicable airspace requirements should not adversely affect the airworthiness or the safe operation of the sailplane. Examples may be PEDs carried by a crew member or a passenger. .

## Slide 12: SUBPART IDE – INSTRUMENTS, DATA AND EQUIPMENT
SAO.IDE.105 Flight and navigational instruments
Regulation (EU) 2018/1976
(a) Sailplanes shall be equipped with a means of measuring and displaying all of the following:
(1) time in hours and minutes;
(2) pressure altitude;
(3) indicated airspeed;
(4) in the case of powered sailplanes, magnetic heading.
(b) In addition to (a), when operating in conditions where the sailplane cannot be maintained on a desired flight path without reference to one or more additional instruments, when conducting cloud flying or when operating at night, sailplanes shall be equipped with means of measuring and displaying all of the following:
(1) vertical speed;
(2) attitude or turn and slip;
(3) magnetic heading.

## Slide 13: SUBPART IDE – INSTRUMENTS, DATA AND EQUIPMENT
SAO.IDE.125 Life-saving and signalling equipment – search and rescue difficulties
Regulation (EU) 2018/1976
Sailplanes operated over areas in which search and rescue (SAR) would be especially difficult shall be equipped with such life-saving and signalling equipment as appropriate to the area overflown.
AMC1 SAO.IDE.125 Life-saving and signalling equipment – search and rescue difficulties
ED Decision 2019/001/R
GENERAL
Sailplanes operated across land areas in which search and rescue would be especially difficult should be equipped with the following:
(a) at least one ELT, one PLB or one equivalent registered emergency locator;
(b) signalling equipment for making distress signals; and
(c) additional survival equipment for the route to be flown taking account of the number of persons on board.

## Slide 14: SUBPART DEC – DECLARATION
SAO.DEC.100 Declaration
Only Commercial operations

## Slide 15: CHAPTER 4 — INITIAL AIRWORTHINESS, CS22
Subpart A — General
Subpart B — Flight
Subpart C — Structure
Subpart D — Design and Construction
Subpart E — Power-plant
Subpart F — Equipment
Subpart G — Operating Limitations and Information
Subpart H — Engines
Subpart J — Propellers